## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
EEG Signal Analysis
During Mental Arithmetic
Group Number: 17
Mattia Pezzano
Maurizio Tirabassi

## Slide 2: Introduction and Experiment Design
Analysis of EEG data to study the differences in brain activity between cognitive engagement and resting conditions
Experiment involving 6 subjects performing serial mental subtraction
Electrodes placed according to the 10-20 International scheme
Brain activity recorded from two phases:
  3-minute rest
  1-minute work
500 Hz sampling frequency

## Slide 3: Material and Methods: Data Preprocessing
The data was provided partially preprocessed:
  0.5Hz high-pass
  45Hz low-pass
  50Hz notch
Trimming the excess of 1000 samples
Extraction of a 45-second window from the middle of the signals:
  Approximation for stationarity
  Good representative portion for each phase
Removal of the mean from the signals

## Slide 4: Material and Methods: Power Spectral Density and Magnitude-Squared Coherence
Power spectral density
Welch method with a 10-second Hamming window with 0.1-second overalp
Baseline-normalization of the work signals with respect to the rest signals
Conversion into decibels
Extraction of the power contribution of relevant frequency bands by integration
Magnitude-squared coherence
Computed between each channel for each frequency band

## Slide 5: Results and Discussion: Frequency Band Activation
Central-parietal beta 2 power increase: stress inducing task and high energy involvement
Parieto-occipital alpha power increase: cognitive load and working memory task
Frontal beta 1 power increase: quiet, focused, introverted concentration and performance increase

## Slide 6: Results and Discussion: Hemispherical Asymmetry in Workload
Asymmetry in frequency band power increase between lobes

## Slide 7: Results and Discussion: Coherence Among Channels During Work
High functional connectivity in the frontal, temporal and central regions: brain areas involved in cognitive engagement